## Slide 1: Low Energy Electronics: DARPA Portfolio
Dr. Michael Fritze
DARPA/MTO
1st Berkeley Symposium on Energy Efficient Electronics Systems
June 11-12, 2009

## Slide 2
Power Efficient Electronics Are Critical
to Many DoD Missions
Soldiers carry packs in 70-120lb range
Frequently 10-20 lbs are batteries!
Dragon Eye
110-200W
Battery Weight 0.7Kg
Power is frequently scarce and expensive: UAVs, remote sensor networks, space, etc.
Getting rid of dissipated heat
is often a major problem by itself!
Heat Pipe

## Slide 3: DARPA Role in Science and Technology

## Slide 4: DARPA Role in Science and Technology
Fritze
Lal Rosker
DARPA PMs work to
“Fill the Gap” with programs
Kenny
Shenoy
Harrod

## Slide 5: DARPA Low Power Electronics
Device Thrust (Fritze, Lal, Shenoy)
STEEP, NEMS, CERA, STT-RAM, “ULP-NVM”
Circuits Thrust (Fritze)
3DIC, “ULP-Sub-VT”, “HiBESST”
Thermal Management Thrust (Kenny)
TGP, MACE, NTI, ACM
“THREADS” (Rosker/Albrecht)
High Performance Computing Thrust (Harrod)
PCA, “EXASCALE”
Programs in BOLD are currently running

## Slide 6: Device Thrust: New Transistor Technology
Electronics History: Power Perspective
It is time for the next paradigm change in transistor technology !
Each technology ultimately reaches integration density limited by power dissipation
Quantum jump then occurs to new technology with lower power

## Slide 7: Steep-subthreshold-slope Transistors for Electronics with Extremely-low Power (STEEP)
GOAL: Realize STEEP slopes
(<< 60 mV/dec) in silicon technology
Platform (Si & SiGe)
PERFORMERS: IBM, UCB, UCLA
APPROACH: BTB Tunneling FETs
“Properly” designed p-i-n device
CHALLENGES:
Abrupt doping profiles !

## Slide 8: Hybrid NEMtronics (Lal)
Objectives
Eliminate leakage power in electronics to enable longer battery life and lower power required for computing.
Enable high temperature computing for Carnot efficient computers and eliminate need for cooling
Approaches
Use NEMS switches with and without transistors to reduce leakage – Ion:Transistor, Ioff: NEMS
NEMS can work at high temperature, enabling high efficiency power scavenging.
N+
N+
P+
P+
N-Well
P-Substrate
VDD
OUT
GND
IN
IN
All Mechanical Computing
Hybrid NEMS/CMOS component integration
Hybrid NEMS/CMOS Device integration
1
1
0
0
1
0
0
1
Ion
Ioff

## Slide 9: NanoElectroMechanical Switches (NEMS)
Berkeley
Argonne
ARL
Block MEMS
CalTech
Case Western
Signal electrode
Actuation electrode
W bridge
Colorado
GE
Minnesota
MIT
Wisconsin
Berkeley
Sandia
Stanford
Performers
Description
Argonne
Diamond/PZT
ARL
PZT/Si Piezoelectric
UC Berkeley
Isolated CMOS Gate
Block MEMS
Multilayer Switch
CalTech
SOI Switch/GaAs Piezo Switch
Case Western
SiC Switch for High T
Colorado
ALD ES Switch
General Electric
Nanorod Vertical Switch
Minnesota
Self-assembled Composite Cantilever Gate
MIT
CNT vertical Switch
Sandia
ALD-deposited High T Material
Stanford
Lateral ES Switch
Wisconsin
Mechanical Motion-based Tunneling

## Slide 10: Carbon Electronics for RF Applications (CERA)
GOALs: Develop wafer-scale epitaxial graphene synthesis techniques. Engineer graphene channel RF-transistors and exploit in RF circuits such as low noise amplifiers
APPROACH: SiC & SiGeC sublimation, CVD, MBE, Nickel catalyzed epitaxy, chemical methods
Performers: IBM, HRL, UCLA
CHALLENGES:
High quality graphene epitaxy
Properly designed G-channel RF-FETs
Si-compatible process flow
Low power high
performance LNAs

## Slide 11: STT-RAM PM: Dr. Devanand Shenoy
Exploit Spin Torque Transfer (STT) for switching nanomagnet orientation to create a non-volatile magnetic memory structure with power requirements 100x lower than SRAM and DRAM, and 100,000x lower than Flash memories
Spin Torque Transfer:
A current spin polarized, by passing through a pinned layer, torques the magnetic moments of the Free layer and switches a memory bit
Ic0
Universal non-volatile magnetic memory with all the advantages and none of the drawbacks of conventional semiconductor memories
 | Program Goal
Write Energy | 0.06 pJ/bit
Write/Read Speed | 5 ns/bit
Cell Area | 0.12 µm2
Thermal stability | 80
Endurance | 3X1016 (cycles)
 | 1 MB memory
MTJ
UCLA

## Slide 12: 3-Dimensional Integrated Circuits (3DIC)
Goal:
Develop 3DIC fabrication technologies and CAD tools enabling high density vertical interconnections
Methods:
3D packaging stacks, wafer-to-wafer bonding, monolithic 3D growth, 3D via technology, CAD tool development
Impact:
3D technologies enable novel architectures with high bandwidth and low latency for improved digital performance and lower power
“HiBESST”
Explore limits of electronic BW
for high speed communication
Compelling 3DIC Demo
Performers: ISC, IBM,
Stanford, PTC
3D FPGA Design & Demos
3D Process
3D CAD
Tezzaron (seedling)

## Slide 13: 3DIC Program

## Slide 14: Ultra-low Power Sub-VT Circuits
Goal: Enable dynamic voltage scaling leveraging sub-threshold operation regime.
Realize minimal performance impact
Challenges: VARIABILITY !
High efficiency low voltage distribution,
Domain granularity, Dynamic voltage/Vtscaling,
Automated CAD tools
IMPACT: Substantial power reduction for key DoD digital computation needs without the need for a novel device technology
Performers: MIT, Purdue, U. Ark,
UVA, Boeing (seedlings)

## Slide 15
chip
chip carrier
(side view)
fan
fin array heat sink
copper
Best modern technology in the electronics layer
Ancient “technology” in the thermal layer !
Microelectronics Packaging Today

## Slide 16
TJunction
Thermal Resistance Breakdown Where is the Problem?
chip carrier
Heat spreader
Si chip
Heat sink
TIM
Temperature
Location
RSubstrate
RGrease
RSpreader
RHeat Sink
TJunction
TTIM
TSpreader
THeatSink
TAmbient
Large DT’s spread throughout path from: Source → Sink
NO SINGLE CULPRIT
Power ~ NCV2F

## Slide 17
TJunction
Thermal Management Portfolio
Temperature
TJunction
TSpreader
THeatSink
TAmbient
Location
RNTI
RTGP
RMACE
Power ~ NCV2F
TTIM
NTI
chip carrier
TGP
chip carrier
Si chip
MACE

## Slide 18: Technologies for Heat Removal from Electronics at the Device Scale (THREADS)
Temperature
TJunction
TSpreader
THeatSink
TAmbient
Location
RNTI
RTGP
RMACE
TTIM
Reduce device-to-substrate thermal resistance
Power
TTHREADS
Repi
Current MTO Programs
“THREADs”
heat spreader
epi
heat sink
TIM

## Slide 19: Exascale Computing Study
What is Needed to Develop Future ExtremeScale Processing Systems ?
Four major challenges identified:
Energy Challenge: Driving the overall system energy low enough so that, when run at the desired computational rates, the entire system can fit within acceptable power budgets.
Parallelism/Concurrency Challenge: Provide the application developer with an execution and programming model that isolates the developer from the “burden” of massive parallelism
Storage Challenge: Develop memory architectures that provide sufficiently low latency, high bandwidth, and high storage capacity, while minimizing power via efficient data movement and placement
Resiliency Challenge: Achieving a high enough resiliency to both permanent and transient faults and failures so that an application can “work through” these problems.
NOTE: Power Efficiency is a Major Challenge !

## Slide 20: Power For Server Farms

## Slide 21: Processor Power Efficiency
“Strawman” processor architecture
  Develop processor design methodology using aggressive architectural techniques, aggressive voltage scaling, and optimized data placement and movement approaches to achieve 10s pJ/flop
  Requires integrated optimization of computation, communication, data storage, and concurrency
Computing Must Be Reinvented For Energy Efficiency
Energy per operation is an overriding challenge
  DATA CENTERS: 1 ExaOPS at 1,000 pJ/OP => GW
    Cost of power: $1M per MegaWatt per year => $1B per year for power alone
  EMBEDDED applications: TeraOPS at 1,000 pJ/OP => KWs
Optimize energy efficiency
Unacceptable
Power Req. !

## Slide 22: Proposed UHPC Program
New system-wide technology approaches to maximize energy efficiency, with a 50 Gigaflops per watt goal, by employing hardware and software techniques for ultra-high performance DoD applications - efficiency.
Develop new technologies that do not require application programmers to manage the complexity, in terms of architectural attributes with respect to data locality and concurrency, of the system to achieve their performance and time to solution goals - programmability.
Develop solutions to expose and manage hardware and software concurrency, minimizing overhead for thousand- to billion-way parallelism for the system-level programmer.
Develop a system-wide approach to achieve reliability and security through fault management techniques enabling an application to execute through failures and attacks.
Goal: Develop 1 PFLOPS single cabinet to 10 TFLOPS embedded module air-cooled systems that overcome energy efficiency and programmability challenges.
Reinventing Computing
For Power Efficiency
Execution Model
UHPC Specifications
1 PFLOPS
50 GFlops/W
Single Air-Cooled Cabinet
10 PB storage
1 PB memory
20 – 30 KW
Streaming I/O
Processor Module
Processor resources & DRAM
10 TFLOPS
32 GB
125 W
1 Byte/FLOP off-chip Bandwidth

## Slide 23: We’re Always Hiring at DARPA
DARPA PM Candidate Characteristics
Idea Generator
Technical Expert
Entrepreneur
Passion to Drive Leading Edge Technology
National Service
DARPA Hires Program Managers for their Program Ideas
… do you have what it takes?
… come talk to us.