## Slide 1
Image Processing for a Point-of-Use Soil Health Assay
Adam Abraham1, Sara Gushgari-Doyle2, Romy Chakraborty2
1Los Angeles Pierce College, Woodland Hills CA
2Ecology Department of Lawrence Berkeley National Laboratory, Berkeley CA
Contact Information
Adam Abraham
Phone: (818) 257-5626
Email: adamabraham14@berkeley.edu
Methods: Object Detection
Introduction
Acknowledgments
The authors would like to thank Nicole McIntyre, Tony Vo Hoang, Sam Mountain, and the E3S staff for facilitating the TTE REU 2021 program and for their constant support. This research was funded by the National Science Foundation Award #1757690.
Abstract
This research provides real-time monitoring of soil health through the improvement of in-field soil health assays. This is accomplished through analyzing colorimetric assays that use pH cresol red to measure the CO2 produced by microbial respiration from prospective soil samples in PCR tubes. We are building an iOS application that processes assay images, analyzes the data, and gives informative feedback on soil health, making it accessible to all via smartphone.
Results
2021 Transfer-to-Excellence Research Experiences for Undergraduates Program (TTE REU Program)
Blur function and cv2.Canny function used to expose contour lines from image
3D Scatter Plot of RGB Pixel Decimal Values
With population rates increasing and growing demands to provide food and energy crops to more people in sustainable ways, soil health has become a priority in solving these challenges
cv2.Rectangle function used to detect edges of well plate
Sample Image Processed: Both Masks Combined
Yellow Mask
We propose a solution with an inexpensive kit that measures soil health effectively
Test more 96-well plate images to increase accuracy in image processing and the standard curve.
Future plates tested will include more values between pH 5 and 6 (e.g. 5.2, 5.4) to create an accurate standard curve between these values.
Future Work
Methods: Accessing Image Pixel Arrays / Data
Red Mask
+
Standard Curves for RGB Channels
A function was used to view and access image pixel arrays and data
This was done to find locations of color pixels
Best Proxy
Sample Image
Blurred Image with Contours
Well Plate Detected
Cropped and Resized Image
Pixel Arrays and Data Exposed